## Slide 1: Evaluation

## Slide 2: Evaluation Metrics for Summarization and Text Generation and must know metrics
Why Evaluation is Needed?
When we create summaries (or translated text), we must measure how good our output is compared to a reference (gold standard).
✅ We don't want to just "feel" that it is good — ✅ We need scientific, quantitative validation.
Metric | What it Measures | Simple Meaning
ROUGE-1 | Overlap of unigrams (single words) between reference and generated text | How many words match?
ROUGE-2 | Overlap of bigrams (two consecutive words) between reference and generated text | How many 2-word sequences match?
ROUGE-L | Longest Common Subsequence (LCS) | How closely the structure/order of words matches?
BLEU | Precision of n-grams (originally for translation, but sometimes used for summarization) | How many generated phrases are correct and match?

## Slide 3: Detailed View of Each Metric
1. ROUGE-1
Checks: Single word matches
Example:
Reference | Generated
"The cat sat on the mat." | "Cat sat on mat."
✅ Common words = {cat, sat, on, mat}
✅ ROUGE-1 score = High
2. ROUGE-2
Checks: Two-word (bigram) sequence matches
Example:
Reference | Generated
"The cat sat on the mat." | "Cat sat on mat."
✅ Common bigrams = {"sat on", "on mat"}
✅ ROUGE-2 score = Medium (Sometimes fewer bigram matches than unigram matches.)

## Slide 4: Detailed View of Each Metric
3. ROUGE-L
Checks: Longest Common Subsequence (LCS)
Example:
Reference | Generated
"The cat sat on the mat." | "Cat sat on mat."
✅ Common subsequence: "cat sat on mat"
✅ ROUGE-L measures how much order is preserved.
✅ Higher if important sentences/phrases are extracted in correct sequence.
4. BLEU (BiLingual Evaluation Understudy)
Checks: Precision of n-grams between generated and reference text.
Mostly used for: Machine Translation originally.
Example:
Reference | Generated
"He is reading a book." | "He reads book."
✅ Partial matches.
✅ BLEU penalizes missing words and wrong word order.
✅ BLEU needs shorter generated text to be very accurate for a higher score.

## Slide 5: When to Use Which Metric
Situation | Best Metric
Summarization (word and phrase match) | ROUGE-1, ROUGE-2, ROUGE-L
Summarization (structure preservation) | ROUGE-L
Machine Translation | BLEU (plus ROUGE sometimes)

## Slide 6: Example
ROUGE Scores for Frequency-Based Summary:
ROUGE1: 0.6624
ROUGE2: 0.6323
ROUGEL: 0.5096
ROUGELSUM: 0.6624
ROUGE Scores for TextRank-Based Summary:
ROUGE1: 0.5417
ROUGE2: 0.5070
ROUGEL: 0.2778
ROUGELSUM: 0.5417

## Slide 7: Interpretation
Metric | Frequency-Based | TextRank-Based
ROUGE-1 | 0.6624 | 0.5417
ROUGE-2 | 0.6323 | 0.5070
ROUGE-L | 0.5096 | 0.2778
ROUGE-Lsum | 0.6624 | 0.5417
Metric | What it Shows | What Your Results Say
ROUGE-1 (unigram overlap) | Measures basic word-level content match | Frequency-based captured more important words.
ROUGE-2 (bigram overlap) | Measures fluency and phrase matching | Frequency-based preserved more 2-word sequences correctly.
ROUGE-L (longest common subsequence) | Measures how well the structure and order is preserved | Frequency-based retained better sentence structure.
ROUGE-Lsum | Measures overall recall | Again, frequency-based is higher — overall better.

## Slide 8: Summary of Interpretation and Recommendation
✅ Frequency-Based Summary:
Captured more words from the reference.
Preserved more meaningful phrases (bigrams).
Maintained better structure.
✅ TextRank-Based Summary:
Captured fewer important words and phrases.
Lower structural match with the reference.
Final Recommendation:
✅ Based on ROUGE-1, ROUGE-2, and ROUGE-L, ✅ the Frequency-Based Summary is statistically better than the TextRank-Based Summary for this particular input text.
🔵 Recommendation:
Prefer Frequency-Based summarization for short, focused, factual paragraphs (like this AI article).
🔵 However:
TextRank may perform better on longer, more diverse documents (e.g., news articles, reports) because it captures sentence-level relationships.